## Slide 1: Performance of ELISA

## Slide 2: HIV ELISA
Enzyme linked immuno sorbant assay-synonymous with EIA (enzyme immuno assay)
On the basis of principle of test ELISA can be:
Indirect ELISA
Direct ELISA
Antigen/antibody capture (sandwich) ELISA
Competitive ELISA

## Slide 3: Indirect ELISA

## Slide 4: Pre ELISA preparations
Study kit insert and prepare SOP
Collect samples
Separate serum and record/log sample as per guidelines
Store in refrigerator (middle shelf and not in the freezer portion)
Ensure that external quality control sample with known acceptable range is available
Ensure Levey Jenning chart is available

## Slide 5: Performance of ELISA 1
Wear lab coat and gloves
Lay down adsorbent sheet with one side plastic on the working bench
Prepare 1% sodium hypochlorite in discards jar
Place materials required (single and multichannel pipettes, disposable 5-50 µl and 50-200 µl tips, SOP of test, ELISA reader washer, Powder less disposable gloves, wash bottles and discards jar, etc.) on the work station

## Slide 6: PERFORMANCE OF ELISA 2
Take out ELISA kit and samples to be tested including external control from the refrigerator and bring to room temperature
Open kit, check expiry date of each component and lay components on work station
Prepare and record details of kit and samples including EQC sample on daily work sheet
Follow the kit instructions and perform all steps of ELISA as per the SOP

## Slide 7: PERFORMANCE OF ELISA 3
Add samples to ELISA plate wells according to schema on the work sheet
Cover the plate and incubate
Prepare wash solution
Set up ELISA Washer
Load the wash solution in the washer
Take out the plate from incubator after recommended time and load onto the ELISA plate washer

## Slide 8: PERFORMANCE OF ELISA 4
Dry the plate after washing
Add conjugate with multichannel pipette
Incubate for the recommended time
Wash and dry the plate
Add substrate using multichannel pipette
Add stopping solution after the recommended time
Shake the plate to mix solution

## Slide 9: PERFORMANCE OF ELISA 5
Load the plate onto the ELISA Reader
Set the plate reading parameters as per kit insert
Take the print out of OD values
Calculate the cut off value as per the kit insert
Interpret the positive and negative result taking into consideration the cut off value
The value of external quality control (EQC sample) should be within range when plotted on Levy Jenning chart for the test run to be valid

## Slide 10: ELISA plate after completion of test