## Slide 1: Collection, Storage and Transport of Blood for HIV Testing
Notes: <number>

## Slide 2: At the end of this module you will be able to:
Understand phlebotomy, the different types of blood sample collection devices, conventional (syringes and needles) and vacuum based tubes
Understand the pre-analytical variables in a diagnostic laboratory which can affect the test results
Understand how to label, store, package and transport (temperature) the specimens
Learn the technique to separate serum from clotted blood
Describe criteria for acceptance/rejection of whole blood specimens
List the necessary information needed for documenting receipt of specimens into the laboratory.
Notes: <number>

## Slide 3: Who should collect blood specimen
Skilled and trained technicians/nurses should collect blood sample
Should use precise procedures for performing phlebotomy and finger prick for collecting the blood specimen as painful, prolonged or repeated attempts at venipuncture can cause pain, discomfort and injury to the patient and result in less than optimum quality or quantity of sample.
Notes: <number>

## Slide 4: Materials required to collect the blood sample
Notes: <number>

## Slide 5: Types of syringes used to collect blood sample
Evacuated tubes, with or without additives (EDTA, etc.) having sufficient vacuum are commercially available and these can be used to draw a predetermined volume of blood.
Red-top tubes contain no additives. These tubes are used to collect blood for tests performed on serum samples (plain vials).
Lavender topped K3EDTA tubes for CD4 testing
Disposable pre-sterilized syringes can also be used to collect blood sample.
Sterilized glass syringes can also be used to collect blood sample
Notes: <number>

## Slide 6: Pre-analytical variables
Specimen collection
Venipuncture: From the vein From the vein
Syringe draw: From the vein
Dermal puncture: From the finger or heel
-(in infants – 6 weeks to 4 months)
Labeling of specimen
Name of the laboratory, name of the client, identifying number, date/time of collection, collectors name,
Notes: <number>

## Slide 7: Collecting blood sample
15
Notes: <number>

## Slide 8: Procedure for drawing blood
16
Introduce yourself and identify the patient (this is the most important point in specimen collection)
Prepare the equipment (needles, tubes, etc.)
Label the vials and verify the same with the patient identification
Wash hands and wear gloves
Prepare the patient (explain the procedure)
1
2
3
4
5
Notes: <number>

## Slide 9: Procedure for drawing blood
17
Apply tourniquet (do not leave it on for more than 1 minute)
Choose a vein
Cleanse the vein and enter and take blood to a full draw(3-5 ml).
If manual method using needle/syringe being used drop sample in container before destroying needle.
Obtain the required amount of blood (3-5ml)
9
8
7
6
Notes: <number>

## Slide 10: Procedure for drawing blood
18
Exit the vein , apply pressure and simultaneously release the tourniquet
Destroy using needle destroyer and discard the needle (in appropriate container)
Invert (mix) the whole blood tubes that contain anticoagulant 6-8 times to avoid clotting/do not invert, allow blood to clot if serum is required for testing
13
11
10
12
Notes: <number>

## Slide 11: Labeling and Test Requisition
19
Labeling of specimen
Patient name or identifying number, date
Name of the test for which drawn
All samples should have a test request form. This should contain the following information:
Name/ ID number of patient, sex
Date and time of sample draw
Clinic name or code
Authorizing clinician
Date and time received and by whom
Specimen accession number
Record of condition of specimen
Specimen type and number of vials
Name and test codes for the tests to be performed
Notes: <number>

## Slide 12
20
Check that Patient Data Matches on Tube and Request Form to minimize pre-analytic mix up of specimens
Clinic should label the tube correctly and double check tube labels and test forms for accuracy in numbering and patient ID before sending to laboratory. The detail on the label should tally with those on requisitioning form
Check Patient Data
Notes: <number>

## Slide 13: Adult and Infant Sample Volumes
21
Samples for adults and older children should be collected by venipuncture preferably using vacuum based safety blood collection tubes.
Samples for younger children are difficult to collect and alternative methods can be used.
All samples should be collected in the correct tube size with the correct amount of anticoagulant
Adult sample
Full draw (3-5ml) blood collected by venipuncture in vacuum-based tube
Infant sample
  0.2 – 0.5 ml whole
  blood collected into Microtainer tube
Notes: <number>

## Slide 14: Blood sample stability for enumeration of CD4 T cells
25
Sample Stability
CD4 count blood samples for the FACS Count are stable for up to 48 hours at room temperature (without refrigeration) before testing*
* This may be prolonged to 72-96 hrs for Calibur and Epics XL
However, laboratory should ideally receive and start testing the sample (stain and fix) within 30 hours of collection in FACS counts
Notes: <number>

## Slide 15: Specimen handling and transport
26
Maintain and transport specimens at the recommended temperature for that test (2 to 8 º C for HIV antibody testing and room temperature 22 to 25º C for CD 4 cell estimation)
Do not refrigerate blood sample to be used for CD4 cell estimation.
Refrigerate the sample to be used for HIV antibody estimation
Avoid extremes in temperatures
Temperatures >370C may cause cellular destruction and affect both hematology and flow cytometry measurements
Notes: <number>

## Slide 16: Specimen handling and transport
27
Always pack the specimen in a leak proof container (e.g., a tube or closed plastic bag) and then in an insulated container with absorbent material to contain an accidental spill
Place absorbent material such as tissue paper or cotton around the tube in the box to ensure that the tube does not move or rattle.
Always keep laboratory requisition papers separate from the specimen container in case of leaks from breakage or spills
Seal the cap of the vacutainer tube with adhesive tape.
Notes: <number>

## Slide 17: Specimen handling and transport
28
Transport by commercial courier or clinic vehicle. Transport is possible by many methods including air, rail, car, bike, motorcycle and hand-carried on foot.
For shipping or transporting the specimens use authorized couriers only. Do not send samples through regular mail.
Declare to the courier that you are shipping an infectious sample.
Transport specimens to the laboratory as soon as possible
Biohazard labels are a must
(FOLLOW IATA GUIDELINES FOR TRANSPORT OF INFECTIOUS SPECIMENS)
Notes: <number>

## Slide 18: Specimen requisition and receipt
29
Record all specimens in a Specimen Identification Log to provide a consistent and complete record of the specimen as well as a way to record workflow numbers (traceability)
All specimens must be accompanied by an appropriate requisition form
Requisition forms should be stored as a record of samples received for testing
Notes: <number>

## Slide 19: Assessment of specimen quality/integrity
30
Inspect the tube and its contents immediately upon arrival, carefully checking for leakage or damage
Reject the specimen and request another if the following occur
The blood is hemolyzed or frozen
Clots are visible
If specimen is > 48 hours old in case of CD4 tests (from the time of draw, check test requisition form for time of draw)
The specimen is improperly labeled (i.e. lacks adequate identification
Notes: <number>

## Slide 20: Assessment of specimen quality/integrity cont.
31
Document the reason for the rejection of any unacceptable specimens or the special handling of specimens
Proper follow up of the problem samples is a must
If the specimen is hot or cold to the touch, or received on ice packs but not obviously hemolyzed or frozen, process it
Note the temperature condition on maintained during the transport on the requisition form and specimen identification log
Notes: <number>

## Slide 21: Summary
32
Sample Collection, such as handling, labeling, processing, aliquoting, storage, and transportation, may affect the results of the study
There must be systematic application of optimum procedures to collect , store and transport the samples so that valid, reproducible, and accurate results are ensured
Notes: <number>

## Slide 22: Summary
33
It is important to follow the test specific requirements for specimen collection
Written policies and procedure regarding specimen collection should be accessible to all personnel in the laboratory and reviewed by the management.
Notes: <number>

## Slide 23: Specimen collection, handling and storage
45
What should be included in a quality assurance SOP covering specimen collection, handling, transport and storage?
Procedures for sample collection, optimal handling conditions for transport and storage should be properly followed
Written procedures with criteria for rejection of unacceptable specimens should be made available to all institutions
Notes: <number>