## Slide 1
1
Biosafety: Practical Considerations
(Use As Reference For Practical)
Notes: <number>

## Slide 2: Objectives
2
Describe the general safety practices to be used in the laboratory
Define what is needed to develop and implement safety policies and training in the laboratory
Describe the PEP Protocols
At the end of this module you will be able to:
Notes: <number>

## Slide 3: Policy for safety in the laboratory
3
Employees themselves for their own protection are responsible for adhering to all biosafety guidelines and regulations set out by the laboratory management as well as demonstrate competency in laboratory safety techniques
Notes: <number>

## Slide 4: Standard Work Precautions
9
Standard work precautions refer to the precautions consistently used on the presumption that all blood and body fluids are potentially infectious for blood borne pathogens.
Similarly, all instruments and other equipment that come in contact with blood are assumed to be potentially infectious and must be properly handled, cleaned, sterilized/ disinfected or safely disposed off.
Notes: <number>

## Slide 5: Standard Work Precautions Include
10
Hand washing with soap & water
Barrier protection. For example effective use of gloves, gowns, masks, goggles, foot cover, etc.
Safe handling of sharp items and prevention of accidents with sharps
Safe handling of specimens (blood etc) during collection, processing and transport
Safe handling of spills of blood
Safe waste disposal
Immunization with hepatitis B vaccine
Lab personnel must observe the standard work precautions as mentioned above
Notes: <number>

## Slide 6: Standard Work Precautions Cont..
11
Take protective measures
Ensure proper use of gloves
Do not touch eyes, nose, mouth or any uncovered body parts, telephone receiver, door handles, tap with gloved hands
Dispose infectious waste in appropriate container
Do not interchange equipment between laboratories
Do not open laboratory doors with gloved hands
Gowns should be closed in front (neck to knees) and with cuffed sleeves
Do not wear open shoes
Notes: <number>

## Slide 7: Hand washing
17
Hand washing is the best defense against all pathogens
Wash hands after handling all materials known or suspected to be contaminated
Good hand washing = 15 seconds with running water, soap, and friction
Notes: <number>

## Slide 8: Effective Hand Washing
18
Notes: <number>

## Slide 9: Effective Hand Washing
19
Area commonly missed in hand washing
Notes: <number>

## Slide 10: Sharps safety
28
Notes: <number>

## Slide 11: Utility of needle cutter and destroyer
35
Minimize the chance of getting injury while collecting blood (needle prick)
Minimize the chance of recycling of the syringe & needles use needle cutter/destroyer) and reduces chance of accidental prick during waste disposal
Do not recap the needles
Notes: <number>

## Slide 12: Splashes to the eye
40
(DEMONSTRATE HOW TO DO IT)
Flush the eye for 5 minutes with clean water (for microorganisms)
Flush at least for 15 minutes (for chemicals)
Notes: <number>

## Slide 13: Commonly used disinfectants in the laboratory
42
Technicians to make/describe how to make?
Ethyl alcohol (70%)
Glutarldehyde (2%)
Sodium hypochlorite solution (1%, 10%)
Polyvidone iodine (pvi) 10%
BIOSAFETY & PEP PROTOCOLS
Notes: <number>

## Slide 14: Recommended strength of the sodium hypochlorite
43
Spills [ 10% ]
Surface contamination
- 1%(smooth surface)
- 10%(porous surface)
Liquid infectious waste (with large amount of organic matter) [ 10% ]
Sharp container for sharps [ 1% ]
Notes: <number>

## Slide 15: Management of spills
45
Put absorbent material down on spillage area
Flood with 10% sodium hypochlorite solution upon & around the spill and leave for 30 minutes
Place the absorbent material in the biohazard bag meant for infectious waste
Reapply the disinfectant solution to all exposed surfaces
Thorough wash of the area with soap and water
Notes: <number>

## Slide 16: Wastes disposal
49
Type of Lab Waste | How to Clean | Where to dispose
Noninfectious/General -ex. Paper, discard reagents, etc. |  | Municipal corporation
Infectious solid |  | Incinerate
Infectious liquid | Disinfect the waste by adding a volume of undiluted sodium hypochlorite solution to the waste so that the final concentration of the diluted sodium hypochlorite solution will be 10% when the container is full. | Flush into sewer
Infectious sharps | Destroy in needle destroyer | Incinerate
Notes: <number>

## Slide 17: Disposal methods
53
Municipal corporation (non infectious material)
Sanitary landfill after decontamination
Deep burial in controlled landfill sites
(if incinerator is not available)
Incinerator (all infectious waste to be incinerated)
All plastic waste is shredded
Notes: <number>

## Slide 18: PEP is not indicated
65
Low risk exposures ex: exposure on intact skin
HIV status of source patient is HIV Negative (no high risk behavior)
Indications determined by case to case
Notes: <number>

## Slide 19: Pre & post test counseling, testing & follow up
66
The HCW should be given pre-test counseling
Reference blood sample to be taken immediately after exposure and tested for HIV antibodies
Blood testing done on 1 and a half months, 3 months and 6 months
Notes: <number>

## Slide 20: PEP medications
68
Basic regimen: Zidovudine (300 mg)+ lamivudine (150mg), 1 tablet twice a day.
Expanded regimen: basic regimen + Nelfinavir 750 mg 8 hourly/Indinavir/Lopinavir/r.
Total duration of PEP 28 days
Recommended to start PEP at the earliest possible, preferably within 2 hours.
Observe for side effects ex. nausea, vomiting, malaise etc.
PEP drugs to be available 24 hours in the healthcare setting.
Guidelines have been sent to all SACs.
Notes: <number>