## Slide 1: PRACTICING IQC DAY-TO-DAY
Introduction to HIV testing
Notes: <number>

## Slide 2: Learning Objectives
The LT will know all the processes and procedures required to perform HIV testing
LT will know the requirements to perform HIV ELISA and Rapid tests following and taking into account all components of quality control (assurance)
The LT will know which controls to include for validation of test results
LT will know how to read, how to calculate, how to interpret the test results
LT will know which testing strategy to follow at ICTC
Notes: <number>

## Slide 3: Requirements for HIV testing laboratory
Ensure that technician is trained to perform the tests
Ensure the materials to be used meet the laid down quality standards and are available
Ensure that environmental conditions are appropriate
Ensure that correct SOPs are available
Ensure that equipment to be used is calibrated
Ensure that standard work precautions and proper waste disposal practices are in place
Notes: <number>

## Slide 4: Procedure
The ELISA/Rapid test kit should be licensed and quality checked and procured by competent authority
The HIV test kit and various components of the kit should not be expired
Use SOP test relevant for the kit used
Take kit out from the refrigerator
Bring kit to room temperature
Notes: <number>

## Slide 5: Procedure Cont.
Include the valid external quality control, internal controls (kit controls) along with test samples for testing (cartridge, comb, ELISA plate etc.)
Prepare daily work sheet, record kit name, lot number, expiry date, date of test, list the samples including the external quality control sample
Label the test devices with client’s ID and one as external quality control
Notes: <number>

## Slide 6: Procedure Cont.
Ensure the correct sample is charged/spotted on to the device/well with the correct number
Try to spot the external quality control for validation of test in the center position/central well among the total samples
Observe right timings for performing various steps of the test
Examine for development of colored dot, line, agglutination, kit control results and read test results
Notes: <number>

## Slide 7: Reading the result
Examine the result of the EQC sample. It should be positive for rapid tests and OD value should be within range for ELISA. Internal controls (kit controls) should perform as per the kit literature.
If above conditions are met, the test performance and test results are valid. If not, test is invalid and has to be repeated.
Notes: <number>