## Slide 1: Performance of HIV rapid tests

## Slide 2: Learning objectives
What are HIV rapid tests?
How to perform HIV rapid tests?

## Slide 3: HIV rapid tests
Rapid tests to detect antibodies to HIV 1 and HIV 2 are in-vitro qualitative tests
Can be performed on whole blood, plasma, serum and saliva. In India whole blood and serum are used
Most rapid test kits come with all materials required to perform the test

## Slide 4: Types of rapid tests
HIV rapid tests can be based on one of the following principles:
Particle agglutination (Latex, RBCs gelatin,)
Immunoconcentration (flow through-vertical, mostly-dot blot assays)
Immunochromatography (mostly-lateral flow)
ELISA based rapid tests-Immunocomb

## Slide 5: Pre-test preparations HIV rapid tests
Study kit insert and prepare SOP
Collect samples
Separate serum and record/log sample as per guidelines/finger prick for test on whole blood
Store in refrigerator (middle shelf and not in the freezer portion)
Ensure that external positive control (QC) sample is available

## Slide 6: Performance of HIV rapid tests 1
Wear lab coat and gloves
Lay down adsorbent sheet with one side plastic on the working bench
Prepare 1% sodium hypochlorite in discards jar
Place materials required (appropriate pipette, Powder less disposable gloves, and discards jar, etc.) on the work station

## Slide 7: Performance of HIV rapid tests 2
Take out the test kit and samples to be tested including external control from the refrigerator and bring to room temperature
Open kit, check expiry date of each component and lay components on work station
Prepare and record details of kit and samples including QC sample on daily work sheet
Follow the kit instructions and perform all steps of the test as per the SOP

## Slide 8: Performance of rapid tests 3
Example Capillus agglutination test:
Take out kit, test samples and positive external control from refrigerator and bring to room temperature
Check the expiry date of all reagents
Organize device on the work bench
Mix the latex reagent
Dispense reagent into mixing well with dropper not touching the surface
Draw sample from vial and dispnse into the latex solution in the device
Allow regent mix to flow through the channel into the viewing window (3-7 minutes)
Read and record result (clumping-positive, no clumping-negative)

## Slide 9: Performance of HIV rapid tests 4
Always put external positive control along side on another device
QC should give positive result
Kit controls should perform as per the kit insert
All above conditions met indicates test performance and results are valid

## Slide 12: UNIGOLD HIV
-Test line present
-Control line present
-Full red spot on sample port
-Control line present
- No test line sen
- Full red spot on sample port